Comparison of Solving Electromagnetic Field Problems with a Computer Using MATLAB and Maple Software

Jeng-Nan Juang

## Abstract

Solving electromagnetic field problems with Maple software was discussed in the ASEE-SE Conference in April of 2000 [1].  Many schools are using their introductory engineering courses to acquaint students with a variety of computer tools and languages. MATLAB has become the technical computing environment of choice for many engineers and scientists. In industrial settings, MATLAB is used for research and to solve practical engineering and mathematical problems. Because the MATLAB computing environment is the one that a new engineer is the most likely to encounter on a job, it is a good tool for an introduction to computing for engineering students.

The main purpose of this paper is to compare the use of MATLAB and Maple software to solve the same problems for electromagnetic fields.

# Introduction

Engineers and scientists use computers to solve a variety of problems, ranging from the evaluation of a simple function to solving a system of nonlinear equations. Because MATLAB is a single interactive system that integrates numeric computation, symbolic computation, and scientific visualization, it has become the choice for the technical computing environment of many engineers and scientists at this time.

In university environments, MATLAB has become the standard instructional tool for introductory courses in applied linear algebra, as well as advanced courses in other fields. There are several electrical engineering text books using MATLAB as the instructional tool [8], [9], [10], [11], [12], [13], [14].

## Theory and Formulas

The same theory and formulas from a previous paper, “Solving Electromagnetic Field Problems with Maple Software,” [1] are used for this paper. The goal of this paper is to demonstrate applications of MATLAB software to static electric fields problems. All the formulas and theory from Coulomb’s law, electrical fields intensity, electric flux density, and Gauss’s law can be solved by MATLAB software.

## Solving Electromagnetic Field Problems

No special knowledge of the MATLAB software interface is required for simple problem-solving, but it is important to type the expressions as they appear on these pages. Three problems from an electromagnetic field textbook [3] have been done in MATLAB to show how it works.

Problem 1:

A charge Qo =  1 nC is located in free space at (a,0,0). Prepare a sketch of the magnitude of the force on Qo, as a function of a (0 ( a ( 5 m), produced by two other charges, Q1 = 1 C at (0,1,0); and Q2 =: (a) 1 C at (0,-1,0); (b) –1 C at (0,-1,0).

The general equation of Coulomb’s Law is given by the mathematical expression:

Where for this problem, Qo = 1 nC at P (a,0,0); Q1 = 1 C at (0,1,0)

- Q2 =  1 C at (0,-1,0),

And

So

(b) Q2 =  -1 C at (0,-1,0),

Using MATLAB to solve the problem:            Using Maple to solve the problem:

x = linspace(0,5)                                                F[a]:=(18*a)/((a^2+1)^1.5);

y = (18.*x)./((x.^2+1).^1.5);                              plot(F[a], a = 0..5);

plot(x,y)

xlabel(‘a’), ylabel(‘F[a]’)

Using MATLAB                                                    Using Maple

x = linspace(0,5)                                                F[b]:=(-18)/((a^2+1)^1.5);

y = (18)./((x.^2+1).^1.5);                                   plot(abc(F[b]), a=0..5);

plot(x,y)

xlabel(‘a’), ylabel(‘F[b]’)

Using MATLAB                                                      Using Maple

x = linspace(0,5)                                                 plot(F[a],abs(F[b])], a = 0..5);

y = (18.*x)./((x.^2+1).^1.5);

z = (18)./((x.^2+1).^1.5);

plot(x,y,x,z)

Using MATLAB                                                       Using Maple

Problem 2:

Let E = (2x + 4y –3)ax + (4x – 2y)ay and: (a) find the equation of the direction line passing through p(1,2,z); (b) sketch this direction line and show E at p.

The equation of a streamline is obtained by solving the differential equation.

And by integrating

Here

So the streamline equation is:

2x2 – 2xy – 2y2 + 3y +4 = 0

solve(%,y)

Solving by MATLAB:                                       Solving by Maple:

x = linspace(-4, 4)                                               y = -1/2*x+3/4+1/4

y = -(1./2).*x+(3./4)+(1./4)                                       *sqrt(20*x^2-12*x+41);

.*sqrt(20.*x.^2-12.*x+41);                            plot(y,x = -4..4);

plot(x,y)

xlabel(‘x’), ylabel(‘y’)

Using MATLAB                                                     Using Maple

Problem 3:

Identical 1-(C point charges are located in free space at (0,0,1) and (0,0,-1). Prepare a plot showing ( E( vs. z along the line x = 0, y = 2, for ( z( ( 10.

Using the formula for Electric Field Intensity:

So

And

Absolute Value for E is:

Solving by MATLAB:

x = linspace(0,10);

y = sqrt([(17980./(4+(x-1).^2).^1.5)+(17980./(4+(x+1).^2).^1.5)].^2+[((8990.*(x-1))./(4+(x-1).^1.5)+((8990.*(x+1))./(4+(x+1).^2).^1.5).^2);

plot(x,y)

xlabel(‘z’), ylabel(‘E(z)’)

Using MATLAB                                            Using Maple

Using Maple to solve the problem:

Restart;

E(y):=17980*(1/(4+(z-1)^2)^1.5)+17980*(1/(4+(z+1)^2)^1.5);

E(z):=8990*((z-1)/(4+(z-1)^2)^1.5)+8990*((z+1)/(4+(z+1)^2)^1.5);

E:=((E(y))^2+(E(z))^2)^(1/2);

Plot(E,Z=0..10)

Conclusion

The main purpose of this paper is to compare Maple and MATLAB software for solving homework problems for Electromagnetic Fields. From the results of the preceding problems, there are no major differences between using MATLAB or Maple for this application. Both have short, easy, equation entry. Both produce clear plots and basic plotting of equations. Both enhance understanding of electromagnetic concepts. There are a few differences to consider, however. Maple shows the equation that has been processed, which allows students to make sure they have the correct solutions; MATLAB does not. MATLAB has simulation (or toolboxes) while Maple has symbolic algebra. The importance of these two differences depends on what the purpose for the application is. For instance, MATLAB can perform simulation for Transfer function as follows:

Step: Apply any value to Transfer Function               Scope: Show the graph of Transfer Function

It is more convenient for engineering students to do the calculation and see the results from the graph through the MATLAB simulation. The final consideration is the difference in cost. Maple student versions cost  $50 each. Each MATLAB student version costs $99; however, to this initial cost one must add $30 for the control tool kit, $30 for the DSP tool kit, and $60 for any other tool kit. Our students must pay more than $250 for the completed student version of MATLAB. Only 25 copies of MATLAB software are installed in our building for students to use. When dealing with students, one should keep their financial obligations in mind.

# References

[1]  Jeng-Nan Juang, (2000) Solving Electromagnetic Field Problems with Maple  Software, ASEE Southeast Section Conference Proceedings (April, 2000).

[2]  DuBroff, Richard E., Stanley V. Marshall, and Gabriel G. Skitek (1996) Electromagnetic Concepts and Applications, Prentice-Hall Inc., New Jersey.

[3]   Hayt, William H., Jr. (1989) Engineering Electromagnetics, McGraw-Hill Inc., New   York.

[4]  Barrow, David, Art Belmonte, Al Boggess, Jack Bryant, Tom Kiffe, Jeff Morgan, Maury  Rahe, Kirby Smith, and Mike Stecher (1998) Solving Differential Equations with Maple V, Brooks/Cole Publishing Company, Pacific Grove, CA.

[5]  Heal, K. M., M. L. Hansen, and K. M. Rickard (1998) Maple V Learning Guide, Waterloo  Maple Inc., Canada.

[6]  Delores M. Etter (1996) Introduction to Matlab for Engineers and Scientists

[7]  User’s Guide for Microsoft Windows (1994) Matlab High-Performance Numeric Computation and Visualization Software.

[8]   Clayton R. Paul [2001] Fundamentals of Electric Circuit Analysis.

[9]   Young W. Kwon, Hyochoong Bang [1997] The Finite Element Method, Using MATLAB.

[10] Frederick/Chow [1995] Feedback Control Problems, Using MATLAB and The Control System Toolbox.

[11] Mark Beale, Howard Demuth [1994] Fuzzy Systems Toolbox, For Use With MATLAB.

[12] Theodore E. Djaferis [2000] Automatic Control, The Power of Feedback.

[13] Fred Taylor, Jon Mellott [1998] Hands-On Digital Signal Processing.

[14] Charles L. Phillips, John M. Parr [1999] Signals, Systems, and Transforms.

## Jeng-Nan Juang

Dr. Juang received the B.S. degree in Electrical Engineering in 1975 from National Taiwan Ocean University, Keelung, Taiwan. The M.S. and Ph.D. degree in 1978 and 1986, respectively, from Tennessee Technological University, TN.

Dr. Juang has been a faculty member of the Electrical & Computer Engineering at Mercer University since 1987.  He served as the head of the Engineering Department at Roane State Community College before he came to Mercer (1980-1987). Dr. Juang has also been serving as Faculty Advisor for the Mercer University NSPE student chapter since 1994. .