Matlab Calculation Software for the Temperature Resolution

Capability of Satellite Radiometer Systems

# Dr. Jeng-Nan Juang,  Salvatore Pino III

Electrical & Computer Engineering

Mercer University

## Abstract

A radiometer is a device used to measure the random signal noise that is emitted by a heated body. The radiometer’s sensor measures the flux of electromagnetic energy reaching it from a predetermined footprint field. The amount of noise released depends on the composition and temperature of the object “seen” by the radiometer antenna. In particular, it measures the absolute temperature of the radiance impinging upon it from a given spectral region of the electromagnetic spectrum. Remote sensors and instruments mounted on satellite systems such as Microwave and Infrared Radiometers have been developed to measure different bands of radiation spectrum, which may carry information about land and sea surface conditions. The series of modeled Brightness Temperatures are calculated by a statistical analysis using Matlab carried out over the entire data set of measurements.

Geostationary satellites provide continuous monitoring of the Earth’s atmosphere and surface. They circle the earth in a geosynchronous orbit on the Earth’s equatorial plane. The orbit matches the Earth’s rotation about its axis. This configuration allows the satellite to continuously view the same areas of the Earth (Winston, 1996). It monitors the Earth’s weather conditions through a predetermined footprint. During normal conditions, observations are taken four times per hour. During severe conditions, observations are taken once per hour through a smaller footprint view. Specifically, it monitors potential severe weather conditions and affects such as tornadoes, flash floods, hail storms, snowfall accumulations, volcano plumes, forest fires and hurricanes. Geostationary satellites have a life expectancy of approximately 5 years.

# Statement and Theory

Satellites in geosynchronous orbit require larger transmission powers, and high gain antenna diameters to overcome the tremendous path loss that takes place as the signal propagates 36,000 km from the Earth to the geosatellite, and vice-versa. The classic link equation for a communications system is represented by equation (A). This illustrates that for a given signal-to-noise ratio (C/N), the transmitter power (Pt) or transmitter gain (Gt) must increase as the path length (S) increases when all other variables are held constant (Larson & Wertz, 1992).

Equation (A):

C/N = [(Pt)(Gt)(Gr)/kTf]]/4S

Gr is the receiver gain

k is the Boltzman constant; 1.380658 x 10

##### T is the system temperature

f  is the receiver bandwidth; the wavelength of the signal

# Brightness Temperature

Brightness Temperature is defined as the amount of radiated energy that is emitted from an object. The brightness temperatures are calibrated by the “tipping curve” calibration procedure (Decker and Schroeder, 1991). The equation to derive atmospheric brightness temperature from the measured voltages and internal temperature is represented by Equation (B). This yields the brightness temperature, Tb.

Equation (B):

X1 is a loss factor

Tw is the temperature of the water vapor in the instrument’s elevation angle (K)

Tr is the temperature of the black body “load” (K)

Th is the temperature of the hot black body (K)

Vr, Vh, and Vm are dc voltage outputs that are proportional to the input power

To  establish a relationship between the brightness temperature and air mass, the brightness temperature at each elevation angle is converted to total absorption, which is linear with mass. This is achieved by using Equation (C) (Wilkinson, 1986). This yields the total absorption, τ.

Equation (C):

Tmr is the mean radiating temperature (K)

Tb is the brightness temperature of the atmosphere (K)

Tbg is the cosmic background radiation; 2.75 K for Tbg

### Radiative Transfer Equation

Radiative Transfer is defined as the process of transmission of the electromagnetic radiation through the atmosphere. The brightness temperature equation that will be used to generate data is to use the height profiles of temperature, water, vapor, and pressure. This is done by evaluating the Radiative Transfer Equation in Equation (D). This equation requires the use of numerical methods for evaluation and it is given by Schroeder and Westwater (1991)

Equation (D):

Tb,v is the brightness temperature (K) at frequency ν

Iv(Tb,v) is the radiance (W m-2 sr-1 GHz-1)

H is the height (Km)

T = T(h) is the temperature (K) at height h

Bv(T) is the planck function (W m-2 sr-1GHz-1)

αν=αν(h) is the absorption coefficient (km-1)

Bν(T) = C1V3/[exp C2V/T-1] (mW/m2/ster/cm-1)

V = # wavelengths in one centimeter (cm-1)

T = temperature of emitting surface (K)

C1 = 1.191066x10-5 (mW/m2/ster/cm-4)

C2 = 1.438833 (cm K)

### Statement of the Problem

The radiometer must resolve temperature changes from one resolution cell to the next when the temperature changes are subjected to a wide variation over its field of view. It must resolve absolute temperatures with a small absolute error to yield accurate tracking data. This paper attempts to prove that using the Radiative Transfer Equation will yield lower brightness temperature, thus improving the accuracy of space radiometers. The main area of concentration is to generate a computer program using Matlab to solve Equation (D). The calculated data from the Radiative Transfer Equation will be compared to the known Brightness Temperatures from the Brightness Temperature Equation at 20.6 GHz, 31.65 GHz and 90.0 GHz. The results will be

summarized in Tables 1, 2, and 3. Additionally, there is a plot in Figure 3 that represents the comparison of the results using the Radiative Transfer Equation to the Brightness Temperature Equation at 20.6 GHz.

Data

The series of modeled Brightness Temperatures are calculated by a statistical analysis using Matlab carried out over the entire data set of measurements. The results using the radiative Transfer Equation are compared to the RTE76, RTE87, and RTE93 models. The results are shown in Figure 1.

Table 1 contains the 209 generated data using the Radiative Transfer Equation  during the first hour and Table 2 contains the 209 generated data using the Radiative Transfer Equation during the last hour. Tables 3, 4, and 5 contain a summary of the results.

Figure 1. Radiative Transfer Equation (D) results plotted against the RTE76, RTE87, and RTE93 models over a 12-Hour Period at 20.6 GHz.

Table 1. The 209 generated data points during the first hour

| 26.699 | 26.710 | 26.720 | 26.730 | 26.740 | 26.750 | 26.760 | 26.770 | 26.780 | 26.790 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 26.800 | 26.810 | 26.820 | 26.830 | 26.840 | 26.850 | 26.860 | 26.870 | 26.880 | 26.890 |
| 26.900 | 26.920 | 26.940 | 26.960 | 26.90 | 27.000 | 27.050 | 27.100 | 27.133 | 27.200 |
| 27.225 | 27.230 | 27.250 | 27.280 | 27.300 | 27.320 | 27.350 | 27.380 | 27.399 | 27.390 |
| 27.380 | 27.370 | 27.360 | 27.350 | 27.340 | 27.330 | 27.320 | 27.310 | 27.300 | 27.290 |
| 27.274 | 27.266 | 27.260 | 27.250 | 27.240 | 27.230 | 27.210 | 27.200 | 27.190 | 27.166 |
| 27.180 | 27.190 | 27.215 | 27.232 | 27.254 | 27.277 | 27.284 | 27.299 | 27.320 | 27.360 |
| 27.374 | 27.380 | 27.399 | 27.390 | 27.386 | 27.380 | 27.373 | 27.370 | 27.368 | 27.366 |
| 27.364 | 27.360 | 27.358 | 27.356 | 27.352 | 27.340 | 27.320 | 27.310 | 27.300 | 27.250 |
| 27.200 | 27.150 | 27.100 | 27.095 | 27.080 | 27.070 | 27.060 | 27.050 | 27.040 | 27.030 |
| 27.020 | 27.010 | 27.005 | 27.000 | 27.010 | 27.030 | 27.045 | 27.060 | 27.075 | 27.090 |
| 27.105 | 27.115 | 27.130 | 27.145 | 27.160 | 27.175 | 27.190 | 27.205 | 27.215 | 27.230 |
| 27.245 | 27.260 | 27.270 | 27.275 | 27.280 | 27.290 | 27.292 | 27.295 | 27.266 | 27.300 |
| 27.300 | 27.295 | 27.290 | 27.280 | 27.276 | 27.270 | 27.260 | 27.245 | 27.230 | 27.215 |
| 27.205 | 27.190 | 27.175 | 27.160 | 27.145 | 27.130 | 27.115 | 27.105 | 27.090 | 27.075 |
| 27.060 | 27.045 | 27.030 | 27.015 | 27.000 | 26.991 | 26.993 | 26.999 | 27.010 | 27.020 |
| 27.030 | 27.050 | 27.062 | 27.050 | 27.042 | 27.040 | 27.000 | 26.990 | 26.980 | 26.970 |
| 26.960 | 26.950 | 26.940 | 26.930 | 26.925 | 26.920 | 26.915 | 26.900 | 26.895 | 26.890 |
| 26.885 | 26.866 | 26.900 | 26.912 | 26.916 | 26.900 | 26.880 | 26.870 | 26.860 | 26.850 |
| 26.840 | 26.830 | 26.820 | 26.810 | 26.800 | 26.790 | 26.780 | 26.770 | 26.760 | 26.750 |
| 26.740 | 26.730 | 26.720 | 26.710 | 26.710 | 26.705 | 26.701 | 26.699 | 26.699 |  |

Table 2. The 209 generated data points during the last hour

| 21.332 | 21.335 | 21.343 | 21.360 | 21.370 | 21.390 | 21.400 | 21.410 | 21.430 | 21.450 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 21.470 | 21.480 | 21.491 | 21.500 | 21.515 | 21.525 | 21.532 | 21.546 | 21.574 | 21.600 |
| 21.613 | 21.629 | 21.642 | 21.660 | 21.682 | 21.699 | 21.700 | 21.715 | 21.723 | 21.731 |
| 21.743 | 21.758 | 21.772 | 21.783 | 21.789 | 21.799 | 21.800 | 21.809 | 21.815 | 21.820 |
| 21.825 | 21.831 | 21.838 | 21.847 | 21.852 | 21.861 | 21.866 | 21.870 | 21.881 | 21.890 |
| 21.894 | 21.899 | 21.885 | 21.880 | 21.860 | 21.830 | 21.800 | 21.790 | 21.770 | 21.745 |
| 21.720 | 21.700 | 21.680 | 21.653 | 21.633 | 21.640 | 21.650 | 21.652 | 21.660 | 21.680 |
| 21.697 | 21.720 | 21.740 | 21.750 | 21.760 | 21.768 | 21.773 | 21.899 | 21.781 | 21.763 |
| 21.751 | 21.743 | 21.731 | 21.720 | 21.713 | 21.704 | 21.693 | 21.688 | 21.678 | 21.671 |
| 21.650 | 21.642 | 21.636 | 21.640 | 21.631 | 21.622 | 21.617 | 21.609 | 21.602 | 21.600 |
| 21.615 | 21.622 | 21.631 | 21.633 | 21.630 | 21.620 | 21.605 | 21.593 | 21.579 | 21.562 |
| 21.548 | 21.531 | 21.524 | 21.518 | 21.510 | 21.500 | 21.490 | 21.480 | 21.467 | 21.458 |
| 21.450 | 21.446 | 21.440 | 21.433 | 21.428 | 21.420 | 21.414 | 21.408 | 21.403 | 21.399 |
| 21.390 | 21.380 | 21.365 | 21.343 | 21.329 | 21.312 | 21.298 | 21.281 | 21.270 | 21.230 |
| 21.200 | 21.163 | 21.112 | 21.103 | 21.081 | 21.042 | 20.993 | 20.981 | 20.970 | 20.961 |
| 20.941 | 20.933 | 20.923 | 20.912 | 20.904 | 20.899 | 20.894 | 20.890 | 20.888 | 20.880 |
| 20.879 | 20.876 | 20.875 | 20.873 | 20.872 | 20.870 | 20.869 | 20.868 | 20.868 | 20.867 |
| 20.868 | 20.861 | 20.853 | 20.847 | 20.841 | 20.832 | 20.829 | 20.813 | 20.807 | 20.800 |
| 20.796 | 20.792 | 20.790 | 20.786 | 20.780 | 20.778 | 20.777 | 20.776 | 20.775 | 20.775 |
| 20.774 | 20.773 | 20.772 | 20.771 | 20.770 | 20.770 | 20.770 | 20.769 | 20.769 | 20.769 |
| 20.769 | 20.768 | 20.768 | 20.768 | 20.767 | 20.767 | 20.767 | 20.766 | 20.766 |  |

Table 3. Comparison of Calculated Brightness Temperature at 20.6 GHz.

| Comparison difference of the Calculated Temperatures to the Models | Difference (K) |
| --- | --- |
| RTE76 | 0.40 |
| RTE87 | 1.48 |
| RTE93 | 0.63 |

Table 4. Comparison of Calculated Brightness Temperature at 31.65 GHz.

| Comparison difference of the Calculated Temperatures to the Models | Difference (K) |
| --- | --- |
| RTE76 | 1.30 |
| RTE87 | 1.96 |
| RTE93 | 0.76 |

Table 5. Comparison of Calculated Brightness Temperature at 90.0 GHz.

| Comparison difference of the Calculated Temperatures to the Models | Difference (K) |
| --- | --- |
| RTE76 | 7.66 |
| RTE87 | 1.95 |
| RTE93 | 1.48 |

Conclusion

Three Brightness Temperature Equations from the RTE76, RTE87, and RTE93 are compared to the Radiative Transfer Equation. At the lower frequency of 20.6GHz, the results are close to the RTE76 (0.40) and RTE93 (0.63) models. There are greater differences when comparing the results to the RTE87 (1.48) model. At the middle frequency of 31.65 GHz, the results are not as good when compared to the three models. The results are closest to the RTE93 (0.76) model. The results compared to the RTE76 (1.30) and RTE87 (1.96) models are approximately 1 and 1.6 times greater than the results produced using the RTE93 model. The results at 90 GHz are not as close as the results at the lower frequencies. The results compared to the RTE76 model yielded the largest difference at 7.66. Additionally, the results compared to the RTE87 model conveyed a smaller difference at 1.95. The results compared to the RTE93 model yielded the smallest difference with a value of 1.48. Regretfully, the Equation (D) model of

Brightness Temperature using the Radiative Transfer Equation does not improve on the

existing RTE76, RTE87 and RTE93 models. The Radiative Transfer Equation of Temperature Brightness does not improve the problem of resolving absolute temperatures from one cell to the next when the radiometer is subjected to a wide variation over its field of view.The primary heading (Heading Style 1) is used to separate major sections of the paper. Notice that there are no columns in this format. Not having columns increases the readability on the CD-ROM. If the paper is submitted in .pdf format, the illustrations can be in color and color can be used in the text to accentuate your points.

When preparing your paper, please use this template as it exists, including all of the predefined styles and headings. This will improve the consistency of the papers in appearance. Papers should be limited to 10 pages in length.

# References

Decker, Martin T., Judith A. Schroeder, Calibration of Ground-Based Microwave Radiometers for Atmospheric RemoteSensing, U.S. Department of Commerce, National Oceanic and Atmospheric Administration, 1991.

England, M. N., F. J. Schmidlin, and J. M. Johansson, Atmospheric Moisture Measurements: A Microwave Radiometer-Radiosonde Comparison, IEEE Transactions on Geoscience Remote Sensing, 31, 389-398, 1993.

Jilla, Cyrus D., Satellite Design: Past, Present and Future, Cambridge, Massachusetts, February 1997.

Han, Yong, J.B. Snider, E.R. Westerman, Observations of Water Vapor by Ground-Based Microwave Radiometers and Raman Lidar, NOAA Environmental Research Laboratory, Boulder, Colorado, 1994.

Hastings, Daniel E. The Technology Drivers Associated With Distributed Satellite Systems, Unpublished Paper, 1996.

Larson, W.L., and J.R. Wertz, Space Mission Analysis and Design, Microcosm Inc., Torrance, California, 1992.

Liebe, H.J. and D. H. Layton, Millimeter Wave Properties of the Atmosphere: Laboratory Studies and Propagation Modeling, NTIA Republic 87-24, National Information Administration, Boulder, Colorado, 74pp., 1987.

Liebe, H. J., G. A. Hufford, and M.G. Cotton, Propagation Modeling of Moist Air and Suspended Water/Ice Particles below1000 GHz, AGARD 52nd Spectroscopic Meeting of the Electromagnetic Wave Propagation Panel, Palma de Mallorca, Spain, 17-21 May, 1993, 3-1 - 3-10, 1993.

Leibe, H. J., P. W. Rosenkranz, and G. A. Hufford, Atmospheric 60-GHz Oxygen Spectrum: New Laboratory Measurementsand Line Parameters, J Quantum Spectroscopic Radiatomospheric Transfer, 48, 629-643, 1992.

Robinson, E. Y., H. Helvajian, and S.W. Janson, Small and Samller: The World of MNT, Aerospace America, September 1996. Pg. 26-32.

Robinson, E.Y., H. Helvajian, and S.W. Janson, Big Benefits From Tiny Technologies, Aweospace America. October 1996.Pg. 38-43.

Rosenkranz, P. W., Interference Coefficients for Overlapping Oxygen Lines in Air, J Quantum Spectroscopic Radiatomospheric Transfer, 39, 287-297, 1998.

University of Alabama, Atmospheric Science Department Homepage:

http://www.atmos.uah.edu/~lerner/satcom/phx_course/instrument/inst_current.htm1

Schroeder, J.S. and E.R. Westwater, Users guide to WPL Microwave Radiative Transfer Software, NOAA Technical Mem.ERL WPL-213, 84pp., 1991.

Sputnik home Page: http://sputnik.infospace.ru/welcome.htm

Virtual Science Center Homepage:

http://www.sci-ctr.edu.sg/ssc/publication/remotesense/meteo.htm

http://www.sci-ctr.edu.sg/ssc/publication/remotesense/mw.htm

Waters, J.W., Absorption and Emission of Microwave Radiation by Atmospheric Gases in Methods of Experimental Physics, vol 12B, edited by M. L. Meeks, Radio Astronomy, Sect. 2.3, 1976.

Wilkinson, D.T., Anisotropy of the Cosmic Blackbody Radiation, Science, 232, 1517-1522, 1986.

Winch, Robert G., Telecommunication Transmission Systems, McGraw-Hill, New York, 1998.

Winston, Wayne G., Interactive Products Branch, Satellite Services Division, NOAA/NESDIS, Camp Springs, Maryland, 1996.

Author1, First Name and First Name Author2 (Year) Book Title, Publisher, Place.

Author1, First Name and First Name Author2 (Year) “Paper Title,” Journal Title, Publisher, Place.

.

## JENG-NAN JUANG

Dr. Juang received the B.S. degree in Electrical Engineering in 1975 from National Taiwan Ocean University, Keelung, Taiwan and the M.S. and Ph.D. degrees in 1978 and 1986 respectively from Tennessee Technological University, Tennessee.  Dr. Juang has been a faculty member of the Electrical and Computer Engineering at Mercer University since 1987.

SALVATORE PINO III

Mr. Pino is a former graduate student under Dr. Juang from Mercer University, majoring in Electrical Engineering.  He graduated in 1999 with an M.S. degree.

# Text boxes

TEMPERATURE (KELVIN)